## Slide 1: FPGA Application on DAQ
2011/5/23
CYC

## Slide 2: Outline
Basic FPGA introduction
NI FPGA modules application on our DAQ
Other information

## Slide 3: FPGA
Field-Programmable Gate Array

## Slide 4
Traditional ASIC Chipset
design=>layout => user
=>single purpose
FPGA Chipset
(design=>write program=>complie)n=>user
=>multi purpose

## Slide 5
FPGA chipset are widely using in various devices
=> ie. CAEN FADC V1724
FPGA program required
=> Verilog or VDHL
NI FPGA program required
=> LabView

## Slide 6: NI FPGA Products
Model | Bus | FPGA Slices | FPGA DSP Slices | Memory (Block RAM) | OnBoard Memory (DRAM)
7965R | PXI-E | 14720 | 640 | 8784Kb | 512MB
7962R | PXI-E | 8160 | 288 | 4752Kb | 512MB
7961R | PXI-E | 8160 | 288 | 4752Kb | 0
7954R | PXI | 17280 | 64 | 4608Kb | 128MB
7953R | PXI | 12960 | 48 | 3456Kb | 128MB
7952R | PXI | 7200 | 48 | 1728Kb | 128MB
7951R | PXI | 4800 | 32 | 1152Kb | 0

## Slide 7
NI-5752 32 Analog In Channels
50 MS/s Sampling Rate
12 bit Resolution
NI-5751 16A I, 8D I/O
50 MS/s Sampling Rate
14 bit Resolution
NI-5761 4A I, 8D I/O
250 MS/s Sampling Rate
14 bit Resolution

## Slide 8: FPGA in DAQ
1. Online PSD
2. Replacing mutli devices

## Slide 9: OnLine PSD
Shrinking HDDs required
=> 30~50Hz data taking Rate
=> 250~450GB/day
Increasing data efficiency
Faster than software online PSD
=> Purely Hardware operation

## Slide 10
Over Threshould
Depending on us
Data Analysing Q&A (parallel Operation)
Trigger out(or not)
Q:sumation
A:Max

## Slide 11: Replacing multi Devices
TDC, Scalar, Hitpttern, Discriminatior

## Slide 12
PMTs(Vetos)
Discriminators(multi devices)
Logic Operation(AND, OR….etc)
Hitpattern
TDC
Scalar
FPGA Modules

## Slide 15: Peer to Peer Communication
40 PMTs for veto,2 inner veto, NaI signal
44 channels separates 2~3 FPGA modules

## Slide 16
PXI-Express Slots

## Slide 17: Additional Information : Design Your Own FPGA Adaptors
Basic XML
VDHL
LabView-FPGA
PCB layout

## Slide 18
End